## Slide 1: Optical Camera Communication (OCC) Video Message Decoding
Problem Understanding Note
Week 1 - Day 1

## Slide 2: 1. Technical Problem Statement
The objective is to decode digital messages transmitted via Optical Camera Communication (OCC).
• Modulation Scheme: On-Off Keying (OOK) to encode binary data into temporal light-intensity variations.
• Goal: Develop a robust, offline, software-based CV and signal processing pipeline.
• Process: Localize transmitter, extract time-series intensity signals, synchronize timing, and reconstruct the binary sequence.
• No physical hardware integration is required.

## Slide 3: 2. Inputs and Outputs
Inputs:
• Raw video sequences capturing the transmitting light source.
• Video frames containing the temporal light-intensity variations.
Outputs/Targets:
• Extracted temporal light-intensity variation time-series signal.
• Decoded transmitted binary sequence (1s and 0s).
• Final reconstructed human-readable decoded message.

## Slide 4: 3. End-to-End Software Pipeline
Pipeline Flow:
  1. Raw Video Input -> 2. Frame Extraction
  3. Transmitter Localization / ROI Selection
  4. Temporal Light Intensity Extraction
  5. Signal Preprocessing & Smoothing
  6. Thresholding / Symbol Classification
  7. Symbol Synchronization & Timing Recovery
  8. Binary Sequence Reconstruction -> 9. Message Decoding
  10. Performance Evaluation & BER Calculation

## Slide 5: Success Criteria
• Accuracy: High accuracy decoding, measured by Bit Error Rate (BER).
• Robustness: Handles varying ROI selections, noise, and ambient lighting.
• Synchronization: Accurate timing recovery to prevent symbol drift.
• Reproducibility: Pipeline must be reproducible, modular, and not heavily hardcoded.

## Slide 6: 4a. Assumptions
1. Sampling Rate: Camera frame rate > Nyquist rate (2x blinking frequency).
2. Spatial Stability: Transmitter remains relatively stationary in FOV.
3. Modulation Scheme: Strictly On-Off Keying (OOK) without complex PWM or multi-level modulation.

## Slide 7: 4b. Technical Questions & Clarifications
1. What is the expected transmission baud rate (blinking freq)?
2. Are there significant rolling-shutter effects we should utilize/avoid?
3. Does the binary sequence include standard start/stop or parity bits?
4. What character encoding standard (ASCII, UTF-8, etc.) is used?
5. Will there be competing ambient light sources or optical noise?