## Slide 1: 1. ROI & Signal Extraction Strategy
Candidate Transmitter ROI Detection:
• Approach: Convert frames to grayscale, apply Gaussian Blur, and use binary thresholding to isolate the brightest region (the LED).
• Draw a fixed bounding box around the centroid of the isolated bright pixels to serve as the ROI.
Intensity Plotting Strategy:
• For every frame, calculate the mean pixel intensity exclusively within the bounded ROI.
• Plot this mean intensity over time (frames) to visualize the raw physical OOK signal.
Name: K.Santhosh Reddy
Cohort: 4 Batch A2
Mentor: Mr. Vamshi

## Slide 2: 2. Synchronization & Evaluation Approach
Symbol Synchronization (260 FPS vs 92 bps):
• Since the camera records at ~260 FPS and transmission is at 92 bps, each transmitted bit spans approximately 2.82 frames.
• We will resample or apply a moving average window of size 3 to smooth the signal and sample the center of each bit period.
Evaluation Criteria:
• Primary Metric: Bit Error Rate (BER) against the expected OOK sequence.
• Secondary Metric: Decoding Accuracy (exact string match of reconstructed text).

## Slide 3: 3. Frozen Preprocessing Plan
The preprocessing pipeline is now frozen as follows:
1. Data Ingestion: Read raw video at native 260 FPS.
2. Grayscale Conversion: Drop RGB channels to reduce computational load.
3. Spatial Localization: Static bright-spot detection on Frame 0.
4. Temporal Extraction: Loop through all frames, appending ROI mean intensity to an array.
5. Output: Save the 1D intensity array (signal) for the modelling phase.
Status: Approved and ready for baseline model implementation.