## Slide 1: Method Comparison (Static vs Adaptive vs Dynamic Phase)
Method | Decoded Correctness | Robustness | Execution Time | Verdict
Static Threshold (Day 11) | Low (fails on drift) | Poor (drifts) | Fastest | Rejected
Adaptive Threshold (Day 15) | Medium (fixes baseline) | Medium (clock drifts) | Fast | Baseline
Dynamic Sync (Day 16) | High | Robust (zero-cross) | Medium | Shortlisted
Name: K.Santhosh Reddy
Cohort: 4 Batch A2
Mentor: Mr. Vamshi

## Slide 2: Discussion: Overfitting, Limitations & Failures
• Overfitting: Tuning the threshold window size (50 frames) heavily to the 1LED video might overfit to its specific lighting drift.
• Data Limitations: Lack of an explicit ground_truth.csv means BER is estimated via internal consistency rather than exact bit matches.
• Complexity: Dynamic phase snapping adds O(N) lookahead searches per frame, increasing processing time compared to static sampling.
• Failure Patterns: Blurring from rapid camera motion causes missed zero-crossings, forcing the decoder to dead-reckon.

## Slide 3: Shortlisted Candidates for Deeper Experiments
Candidate 1: Dynamic Sync Decoder (Adaptive Threshold + Zero-Cross Snapping)
- Rationale: Only method currently capable of extracting 10,000+ stable bits from the drifting 1LED video.
Future Enhancements for Candidate:
- Implement a Phase-Locked Loop (PLL) to handle missed zero-crossings gracefully instead of dead-reckoning.
- Test multi-channel (RGB) thresholding rather than pure grayscale intensity to improve resilience against color temperature changes.